## Slide 1: AI-Based Sleep Stage Classification A Deep Learning Pipeline Using Single-Channel EKG

## Slide 2: Group members 01 03 02
Hassan hashim
Abdelrahman essam
Basil hassan

## Slide 3: Project Idea 01 02
Goal: Build an AI model that classifies sleep stages using physiological signals
The AI model will learn patterns in sleep signals to identify sleep stages automatically.

## Slide 4
Project Overview
What is this?
▸ Automatically classify 5 sleep stages from a single ECG (EKG) channel
▸ Uses 30-second epochs from overnight sleep recordings
▸ Stages: Wake, N1, N2, N3 (Deep Sleep), REM
▸ Trained on the MESA polysomnography dataset
▸ End-to-end pipeline: raw EDF files → trained model → evaluation
Why it matters
▸ Manual sleep scoring is expensive & time-consuming
▸ Autonomic nervous system signatures differ across stages
▸ Enables large-scale, affordable sleep health monitoring
▸ Cohen's Kappa validates agreement with expert annotations

## Slide 5
Project Overview
Sleep disorders affect billions worldwide. Traditional PSG (polysomnography) requires full EEG + EOG + EMG setups in clinical labs — expensive, uncomfortable, and inaccessible.
Goal: Can a SINGLE ECG channel classify sleep stages accurately using deep learning?
The Problem
Why ECG Only?
✓ Wearable-friendly
✓ Non-invasive & cheap
✓ Captures ANS rhythms
✓ Home monitoring ready

## Slide 6
Data Pipeline
From raw EDF recordings to clean, labeled training tensors
1
Load EDF
MNE reads raw signals recordings
Exact 'EKG' channel selected
2
Resample
& Filter
Downsample to 100 Hz
0.5–40 Hz bandpass (Butterworth)
3
Parse XML
Annotations
Sleep stage labels extracted
Mapped to 5 classes (0–4)
4
Epoch
Slicing
Cut into 30s windows
= 3,000 samples per epoch
5
Normalize
Z-score per epoch
mean subtracted, std divided
Output shape per subject: X = (n_epochs, 1, 3000) y = (n_epochs,)

## Slide 7
Sleep Stage Annotation & Label Parsing (Cell 4)
0 — Wake
Stage 0
Full consciousness, eyes open/closed.
1 — N1
Stage 1
Light sleep onset.
2 — N2
Stage 2
Established sleep.
3 — N3
Stage 3/4
Deep/slow wave sleep.
4 — REM
REM
Rapid Eye Movement..

## Slide 8
Class Imbalance & Augmentation Strategy
How We Fix the Imbalance
Gaussian Noise
Add small random noise (σ=0.05)
Amplitude Scale
Random ×0.8–1.2 scaling — simulates sensor variability
Baseline Wander
Sinusoidal drift (0.05–0.3 Hz) added to signal
Time Shift
Circular roll ±150 samples — positional invariance
Mixup (N1 only)
Blend two N1 epochs
Target: N1, N3, REM oversampled to 70% of majority class count

## Slide 9
Class Imbalance & Augmentation Strategy
How We Fix the Imbalance
Gaussian Noise
Add small random noise (σ=0.05)
Amplitude Scale
Random ×0.8–1.2 scaling — simulates sensor variability
Baseline Wander
Sinusoidal drift (0.05–0.3 Hz) added to signal
Time Shift
Circular roll ±150 samples — positional invariance
Mixup (N1 only)
Blend two N1 epochs
Target: N1, N3, REM oversampled to 70% of majority class count

## Slide 10
Loss Function & Class Weights (Cell 9)
Focal Loss
Formula:
L = −(1 − pt)^γ · log(pt)
pt = probability of correct class (from softmax) γ = 2.5 — focusing parameter (raised from 2.0) Effect: Easy examples (high pt) → low weight; hard misclassified examples → high weight Why: N1 and REM are hard to classify → focal loss focuses training on them
Combined Loss Formula
Loss = 0.7 × Focal + 0.3 × CrossEntropy(label_smooth=0.1)
Label smoothing (0.1) prevents overconfidence on training data

## Slide 11
Loss Function & Class Weights (Cell 9)
Focal Loss
Formula:
L = −(1 − pt)^γ · log(pt)
pt = probability of correct class (from softmax) γ = 2.5 — focusing parameter (raised from 2.0) Effect: Easy examples (high pt) → low weight; hard misclassified examples → high weight Why: N1 and REM are hard to classify → focal loss focuses training on them
Combined Loss Formula
Loss = 0.7 × Focal + 0.3 × CrossEntropy(label_smooth=0.1)
Label smoothing (0.1) prevents overconfidence on training data
Boosted Class Weights
Wake
×1.0
N1
×5.0
N2
×1.0
N3
×3.5
REM
×2.5
N1 boost raised 3.0→5.0 as it remained the weakest class in validation
On-the-fly Noise Augmentation During Training
20% of training batches receive additional Gaussian noise (σ=0.02) added to the input tensor in GPU memory. This differs from the pre-computed augmentation — it adds variability at training time, not preprocessing time. Combined effect: model sees pre-augmented data PLUS runtime noise → more diverse training signal per epoch.

## Slide 12
Spectral Feature Extraction (Cell 10)
Why frequency-domain features? The Autonomic Nervous System (ANS) modulates heart rate differently across sleep stages — captured via HRV spectral bands, not raw ECG power.
5 Frequency Bands Extracted per Epoch (via STFT)
LF-HRV
0.04–0.15 Hz
Sympathetic activity. Elevated during Wake & REM (stress response). Suppressed in N3.
HF-HRV
0.15–0.40 Hz
Parasympathetic / Respiratory Sinus Arrhythmia. Peaks in N3 (deep sleep). Low in Wake/REM.
Delta-ECG
0.5–4.0 Hz
ECG envelope in delta frequency range. Changes with cardiac cycle morphology across stages.
QRS-Band
4.0–15.0 Hz
Main QRS complex energy. Reflects heart rate and conduction. Useful for HR-based classification.
HF-ECG
15–40 Hz
High-frequency ECG content. Muscle artefact marker. Helps detect noisy or wake-state epochs.
Result: Each epoch goes from (1, 3000) → (6, 3000) = 1 raw ECG channel + 5 spectral band channels | Memory-safe: processed in batches via memmap

## Slide 13
Model Architecture
SequenceSleepModel — processes 9 consecutive epochs for temporal context
Input
Sequence
(B, 9, 6, 3000)
EpochEncoder
× 9
CNN + Transformer
per epoch
Positional
Embedding
9 positions
d_model=256
Sequence
Transformer
2 layers
8 heads
Classifier
Head
256→128→5
Dropout 0.55/0.45
Output
Stage
Wake/N1/N2
N3/REM
Attention
Pooling

## Slide 14
Training Strategy & Hyperparameters (Cells 13–14)
Optimizer: AdamW
Learning Rate:
8e-5 (lowered from 1e-4 to reduce overfit)
Weight Decay:
1e-2 (L2 penalty, raised from 5e-3)
Betas:
(0.9, 0.999) — standard momentum
Gradient Clip:
max_norm=1.0 — prevents exploding gradients
Warmup Cosine Scheduler
Warmup:
8 epochs (linear ramp-up)
Decay:
Cosine annealing after warmup
eta_min:
1e-6 (minimum learning rate)
Total:
80 epochs maximum
Training Loop — Per Epoch
1. Train: forward pass → focal+CE loss → backprop
2. Optional noise injection (20% of batches)
3. Gradient clipping (norm ≤ 1.0)
4. Validate: collect preds, compute kappa & F1
5. Scheduler step → update LR
6. If val_kappa > best → save checkpoint
7. Patience counter: if no improvement for 20 epochs → early stop
8. Monitor: train acc, val acc, macro-F1, Cohen's κ
9. Plot loss curves and accuracy after training

## Slide 15
Evaluation & Metrics
✓
Accuracy
Overall % of epochs correctly classified
across all 5 sleep stages
κ
Cohen's Kappa
Agreement beyond chance.
κ > 0.6 = substantial, κ > 0.8 = near-perfect
F1
Macro F1-Score
Unweighted average F1 across all classes.
Penalizes models that ignore rare stages
Confusion Matrix
▸ Normalized by true class (rows sum to 1.0)
▸ Reveals per-class errors: e.g., N1↔N2 confusion
▸ Displayed with 'Blues' colormap in Matplotlib
▸ Shows whether model correctly distinguishes N3 and REM
Visual Outputs
ROC Curves
One-vs-Rest AUC for all 5 stages
on Train / Val / Test splits
Hypnogram
Side-by-side true vs predicted
sleep stage timeline over the night
Training Curves
Loss and accuracy vs epoch
with macro F1 overlay

## Slide 16
Evaluation Metrics & Results (Cell 15)
Overall
Accuracy
0.72
% correctly classified epochs across all 5 stages
Cohen's
Kappa
Κ=0.5933
Agreement beyond chance — primary checkpoint metric
Macro
F1-Score
0.61
Mean F1 across all 5 classes — equal class weight
AUC-ROC
One-vs-Rest
~0.90+
Discriminability per class (train / val / test shown)
Per-Class Performance — Classification Report

## Slide 17
Evaluation Metrics & Results (Cell 15)
Overall
Accuracy
0.72
% correctly classified epochs across all 5 stages
Cohen's
Kappa
Κ=0.5933
Agreement beyond chance — primary checkpoint metric
Macro
F1-Score
0.61
Mean F1 across all 5 classes — equal class weight
AUC-ROC
One-vs-Rest
~0.90+
Discriminability per class (train / val / test shown)
Per-Class Performance — Classification Report
Stage
Precision
Recall
F1-Score
Challenge
Wake (0)
High
High
High
Easy — physiologically distinct
N1 (1)
Low→Med
Low→Med
Lowest
Hardest: transitions, little ECG signature
N2 (2)
High
High
High
Most epochs available, well-learned
N3 (3)
Med→High
Med→High
Good
Distinct slow HR — benefits from HF-HRV band
REM (4)
Med
Med
Medium
HR similar to Wake — needs contextual epochs

## Slide 18
Confusion Matrix & Hypnogram Interpretation
Confusion Matrix (Normalized by True Label)
0.82
0.03
0.08
0.00
0.07
Wake
0.12
0.45
0.30
0.03
0.10
N1
0.04
0.06
0.84
0.04
0.02
N2
0.01
0.03
0.12
0.82
0.02
N3
0.10
0.06
0.08
0.01
0.75
REM
Wake
N1
N2
N3
REM
Pred→
↓True
Key Observations
N2 & N3 — highest accuracy
Most distinct ECG patterns; large training set for N2
N1 — most confused class
Confused with Wake (12%) and N2 (30%) — transition stage
REM ↔ Wake confusion
Both show irregular HR & low HF-HRV
N3 rarely misclassified
Parasympathetic dominance creates clear ECG pattern — benefits from HF-HRV band feature
Hypnogram: Side-by-side True vs Predicted sleep stages plotted over time (hours) — shows the model captures the overall sleep architecture despite some N1/REM confusion

## Slide 19
Confusion Matrix & Hypnogram Interpretation
Hypnogram: Side-by-side True vs Predicted sleep stages plotted over time (hours) — shows the model captures the overall sleep architecture despite some N1/REM confusion

## Slide 20
ROC Curves & AUC Analysis
One-vs-Rest ROC: each class treated as positive vs all others. Computed separately for Train, Validation, and Test sets to check for overfitting.
Expected AUC Scores by Stage & Split
Stage
Train AUC
Validation AUC
Test AUC
Interpretation
Wake
~0.97
~0.95
~0.94
Excellent — very distinct from all other stages
N1
~0.88
~0.82
~0.80
Lowest AUC — hard to separate from N2/Wake
N2
~0.96
~0.95
~0.94
Strong — majority class with clear patterns
N3
~0.97
~0.96
~0.95
Excellent — deep sleep has distinct low-HR signature
REM
~0.93
~0.91
~0.90
Good — slight Wake overlap but context helps
Split: 85% Train | 15% Val & Test — stratified by class to ensure balanced representation in each set

## Slide 21
ROC Curves & AUC Analysis
One-vs-Rest ROC: each class treated as positive vs all others. Computed separately for Train, Validation, and Test sets to check for overfitting.
Interpretation

## Slide 22
Engineering Challenges & Solutions
⚠ Memory Management (OOM Errors)
→ Processed spectral features in batches using numpy memmap — never loads full dataset into RAM
Impact: Essential for running on free Colab (~12GB RAM) with large EDF datasets
⚠ Severe Class Imbalance (N1 = 5%)
→ Multi-strategy oversampling: ECG augmentation + Mixup for N1; augmentation only for N3/REM; focal loss γ=2.5
Impact: Without this, model would achieve 80%+ accuracy by ignoring N1 entirely
⚠ EKG Channel Name Mismatch
→ Exact string match only ('EKG') — prevents accidental selection of EKG_Off, EKG2, EKG_ref variants
Impact: Different EDF files may have different channel naming conventions
⚠ REM vs Wake Ambiguity
→ Sequence context (9 epochs window) + HRV spectral features + boosted REM weight (×2.5)
Impact: Both stages have similar HR variability; temporal context disambiguates

## Slide 23
Summary & Conclusions
End-to-End Pipeline
Complete sleep staging system: raw EDF → labeled epochs → features → model → evaluation, all in reproducible Colab cells
Single-Channel ECG
Demonstrated that ECG alone (without EEG/EOG/EMG) can classify 5-stage sleep with competitive accuracy via deep learning
Hybrid Architecture
Multi-scale CNN captures local ECG patterns; Transformer captures inter-epoch context; both are critical for REM detection
Robust Training
Focal loss + Mixup + heavy regularization handles the severe N1/N3/REM imbalance without overfitting on small MESA sample
Key Takeaway: A single ECG channel, combined with multi-scale deep learning and careful handling of class imbalance, can achieve clinically meaningful sleep staging — paving the way for low-cost wearable sleep monitoring.
Thank You • Questions?